## Slide 1: ENHANCED CLUSTERING AND ROUTING MECHANISM FOR ENERGY EFFICIENT COMMUNICATION IN WIRELESS SENSOR NETWORKS
Presented by: Under the guidance of :
SRINATH S ( 2024616026) Dr. VASIM BABU
M.E Wireless Technologies. Assistant Professor,
Dept of Electronics Engineering,
Madras Institute of Technology,
Anna University.
DEPARTMENT OF ELECTRONICS ENGINEERING
MIT CAMPUS, ANNA UNIVERSITY
PROJECT WORK I

## Slide 2
CONTENTS
Objective
Proposed Methodology
Flow Chart
Work flow
Result and Discussion
References

## Slide 3
OBJECTIVE
The project aims to develop a novel, clustering algorithm and a resource-aware routing protocol.
The proposed clustering will achieve balanced workload distribution and mitigate hotspots, enhancing network lifetime.
The routing protocol aims to enable real-time adaptation with minimal re-clustering and low communication overhead.
An optimized hybrid algorithm, combining clustering and routing, will be validated through simulations and hardware testing for superior performance.

## Slide 4
Clustering organizes sensor nodes into smaller groups to manage communication efficiently.
Each cluster has a Cluster Head (CH) responsible for coordination.
Normal nodes, called Cluster Members (CMs), send their sensed data to the CH.
The CH aggregates and compresses the collected data.
Aggregated data is then transmitted from CHs to the Base Station (BS).
This approach reduces energy consumption and extends the overall network lifetime.
Clustering in WSN

## Slide 5
Direct communication of every node with BS causes high energy consumption.
Nodes far from BS die quickly due to long transmission distances.
Random CH selection may overload weak nodes and reduce network lifetime.
CH selection ensures efficient energy distribution among all nodes.
Extends network lifetime by reducing energy drain.
Maintains connectivity by preventing early node deaths.
Improves scalability for large networks.
Cluster Head Selection

## Slide 6
PROPOSED METHODOLOGY
Hybrid ISSA+PSO
Improved Squirrel Search Algorithm(ISSA)
The Improved Squirrel Search Algorithm (ISSA) is a nature-inspired metaheuristic based on the gliding and food-searching behavior of flying squirrels.
Key mechanisms in ISSA:
Adaptive Population Initialization: generates initial solutions closer to optimal regions,
Dynamic Step Size Control: adaptively adjusts the search step to balance exploration of new solutions and exploitation of good ones.
Local Search Mechanism: refines promising solutions through neighborhood search for higher accuracy.
Seasonal Monitoring & Lévy Flight: help ISSA avoid local optima and explore globally.

## Slide 7
ISSA selects CHs based on multiple criteria:
  Residual Energy (): Prefer nodes with higher energy.
  Where is CH’s current energy
  Intra-cluster Distance (): Minimize member-to-CH distance.
  where Distance among sink and CHj
  No. of SNs in the cluster j
  Sink Distance (): CH closer to BS is preferred.
  where Distance between CHj and BS
ISSA for Cluster Head Selection

## Slide 8
  Cluster Balance Factor (f4): Maintain equal cluster sizes.
  Where n is overall number of live SNs
  m - overall number of CHs
  Fitness function:
where a, b, and c are constant values and a + b + c = 1
ISSA for Cluster Head Selection

## Slide 9
Energy model
Transmission energy
where is Data packet length (in bits)
is Circuitry energy
Free space amplification energy
Multipath fading amplification energy
Reception Energy
Total Energy

## Slide 10
Particle swarm optimization algorithm
PSO is a population-based metaheuristic inspired by the social behavior of bird flocking and fish schooling.
Each potential solution is called a particle, represented by a position and velocity in a search space.
Particles move by updating their position based on:
  Their own best experience (pbest)
  The global best solution found by the swarm (gbest)

## Slide 11
Particle swarm optimization algorithm
Particle position
Particle velocity
Best local position
Position update rule
Velocity update rule
Where | 
Xi | Particle ii's position vector
Vi | Particle ii's velocity vector
pi | Particle ii's personal best position
pbesti | Best-known position for particle i
gbest | Best-known position for the entire swarm
c1,c2 | Cognitive & social coefficients
ri1,ri2 | Random numbers for stochastic effect
D | Dimensionality of the problem

## Slide 12: FLOW CHART
Start
End
No
Yes

## Slide 13: Pseudo code of the proposed Method
Start Hybrid ISSA+PSO
1. Create random population of solutions
2. Calculate fitness of each solution
3. Save best solution of each candidate (pbest)
4. Save overall best solution (gbest)
Repeat until maximum iterations:
For each candidate:
- Move using ISSA rules (towards gbest, random reset, local search )
- Move using PSO rules (velocity + position update)
- Compare both moves, keep the better one
- Update pbest if improved
Update gbest (best among all pbests)
End Repeat
Return gbest as final best solution
End Hybrid ISSA+PSO

## Slide 14
RESULT AND DISCUSSION

## Slide 15
SIMULATION PARAMETERS
Area | 200*200
Base Station Position (scenario 1) | (100,100)
Base Station Position (scenario 2) | (0,0)
No. of Sensor nodes | 100,200,300
Initial energy per node | 4 J
Percentage of CHs | 5%
Transmission Range | 90 m
Packet size | 640 bytes
Area | 
Base Station Position (scenario 1) | (100,100)
Base Station Position (scenario 2) | (0,0)
No. of Sensor nodes | 100,200,300
Initial energy per node | 4 J
Percentage of CHs | 5%
Transmission Range | 90 m
Packet size | 640 bytes

## Slide 16
SIMULATION SETUP

## Slide 17: Network Life Time
Chart: Base Station (100,100)- Scenario 1
| ISSA | ISSA+PSO | ISSA | ISSA+PSO | ISSA | ISSA+PSO | 100 Nodes | 200 Nodes | 300 Nodes
First Node Death | 3390 | 3584 | 4116 | 4763 | 3468 | 4258
Half Node Death | 6302 | 6382 | 7027 | 7170 | 7383 | 7518
Last Node Death | 7726 | 8078 | 8519 | 8534 | 9047 | 9308

## Slide 18: Network Life Time
Chart: Base Station (0,0)- Scenario 2
| ISSA | ISSA+PSO | ISSA | ISSA+PSO | ISSA | ISSA+PSO | 100 Nodes | 200 Nodes | 300 Nodes
First Node Death | 1727 | 1931 | 1649 | 1881 | 1346 | 1809
Half Node Death | 4636 | 4657 | 4861 | 4897 | 5086 | 5105
Last Node Death | 9203 | 8965 | 10296 | 10266 | 10670 | 10319

## Slide 19: Total Residual Energy
Chart: ISSA (Existing)
| 0 | 1000 | 2000 | 3000 | 4000 | 5000 | 6000 | 7000 | 8000 | 9000 | 10000
scenario 1 node= 100 | 400 | 335 | 270 | 205 | 141 | 82 | 32 | 4.5 | 0 | 0 | 0
scenario 2 node= 100 | 400 | 315 | 220 | 144 | 75 | 31 | 11 | 4 | 1.05 | 0.07 | 0
scenario 1 node= 200 | 800 | 677 | 561 | 450 | 327 | 218 | 110 | 34 | 0.58 | 0 | 0
scenario 2 node= 200 | 800 | 619 | 453 | 303 | 175 | 82 | 33 | 11.67 | 2.5 | 0.5 | 0.07
scenario 1 node= 300 | 1200 | 1031 | 863 | 695 | 524 | 363 | 218 | 96 | 13 | 0.0156 | 0
scenario 2 node= 300 | 1200 | 946 | 698 | 475 | 273 | 147 | 66 | 26 | 8.6 | 2 | 0.023

## Slide 20: Total Residual Energy
Chart: ISSA+PSO (Proposed)
| 0 | 1000 | 2000 | 3000 | 4000 | 5000 | 6000 | 7000 | 8000 | 9000 | 10000
scenario 1 node= 100 | 400 | 331 | 267 | 205 | 140 | 83 | 36 | 8.89 | 0.104 | 0 | 0
scenario 2 node= 100 | 400 | 314 | 226 | 146 | 79 | 31 | 12 | 3.6 | 0.8 | 0 | 0
scenario 1 node= 200 | 800 | 684 | 566 | 451 | 336 | 214 | 110 | 37 | 2.26 | 0 | 0
scenario 2 node= 200 | 800 | 620 | 457 | 296 | 169 | 83 | 33 | 10 | 2.3 | 0.36 | 0.069
scenario 1 node= 300 | 1200 | 1032 | 849 | 688 | 527 | 356 | 208 | 90 | 14 | 0.121 | 0
scenario 2 node= 300 | 1200 | 940 | 690 | 466 | 279 | 148 | 67 | 25 | 8.08 | 1.32 | 0.1492

## Slide 21: WORK FLOW
Review | Work to be Done
Review 1 | Technical Modeling, Algorithm Development and Simulation For Clustering.
Review 2 | Algorithm Development & Simulation for Routing
Review 3 | Comparative Analysis and Hardware Testing

## Slide 22: REFERENCES
[1] Alshammri, G.H. Enhancing wireless sensor network lifespan and efficiency through improved cluster head selection using improved squirrel search algorithm. Artif Intell Rev 58, 79 (2025). https://doi.org/10.1007/s10462-024-11088-4.
[2] Shafiq Alam, Gillian Dobbie. et al. Research on particle swarm optimization based clustering: A systematic review of literature and techniques, in Elsevier 2014 Swarm and Evolutionary Computation, Volume 17,Pages 1-13 https://doi.org/10.1016/j.swevo.2014.02.001
[3] Tawfeek, M.A., Alrashdi, I., Alruwaili, M. et al. Improving energy efficiency and routing reliability in wireless sensor networks using modified ant colony optimization. J Wireless Com Network 2025, 22 (2025). https://doi.org/10.1186/s13638-025-02449-w
[4] C. Wang, X. Liu, H. Hu, Y. Han and M. Yao, "Energy-Efficient and Load-Balanced Clustering Routing Protocol for Wireless Sensor Networks Using a Chaotic Genetic Algorithm," in IEEE Access, vol. 8, pp. 158082-158096, 2020. doi: 10.1109/ACCESS.2020.3020158.
[5] Roy, K.; Kim, M.-K. Applying Quantum Search Algorithm to Select Energy-Efficient Cluster Heads in Wireless Sensor Networks. Electronics 2023, 12, 63. https://doi.org/10.3390/electronics12010063

## Slide 23: REFERENCES(Cntd.)
[6] D. Gupta et al., "Optimizing Cluster Head Selection for E-Commerce-Enabled Wireless Sensor Networks," in IEEE Transactions on Consumer Electronics, vol. 70, no. 1, pp. 1640-1647, Feb. 2024, doi: 10.1109/TCE.2024.3360513.
[7] M. Biradar and B. Mathapathi, ‘‘Secure, reliable and energy efficient routing in WSN: A systematic literature survey,’’ in Proc. Int. Conf. Adv. Electr., Comput., Commun. Sustain. Technol. (ICAECT), Feb. 2021, pp. 1–13, doi: 10.1109/ICAECT49130.2021.9392561
[8] M. Shafiq, H. Ashraf, A. Ullah, and S. Tahira, ‘‘Systematic literature review on energy efficient routing schemes in WSN—A survey,’’ Mobile Netw. Appl., vol. 25, no. 3, pp. 882–895, Jun. 2020.
[9] O. A. Khashan, R. Ahmad, and N. M. Khafajah, ‘‘An automated lightweight encryption scheme for secure and energy-efficient communi cation in wireless sensor networks,’’ Ad Hoc Netw., vol. 115, Apr. 2021, Art. no. 102448.
[10] S. Umbreen, D. Shehzad, N. Shafi, B. Khan, and U. Habib, “An energy efficient mobility-based cluster head selection for lifetime enhancement of wireless sensor networks,” IEEE Access, vol. 8, pp. 207779–207793, 2020, doi: 10.1109/ACCESS.2020.3038031.

## Slide 24: THANK YOU